## Slide 1: 1. Download LORECa Fitting Software Version 4.3.1
1.1 - Download the LORECa 4.3.1 fitting software from the website. And complete the installation.
1.2 - Connect the hearing aid and PC with Hi-pro.
1.3 - Insert the programming cable for either the left ear or the right ear. Make sure Hi-pro is connected to the computer and the device is working and click programming software.

## Slide 2: 2. Customer information entry.
2.1 - If you have previously saved patient information in this software, click on the patient to select the current patient.
2.2 - If you are going to add a new patient, you can open a new patient record by double clicking on an empty line.

## Slide 3
2.3 - Fill in the information such as the patient's name, gender, age and date of purchase and click OK.
2. Customer information entry.

## Slide 4
2.5 - With the relevant patient selected, click the Audiogram section on the left.
2. Customer information entry.

## Slide 5
2.5 - Create the patient's audiogram using the mouse. You can detail the audiogram you draw with red for the right ear, and blue for the left ear, using the ACL, BCL and UCL options. If you wish, you can copy the graphic on the right to the left and the graphic on the left to the right using the Copy option.
2. Customer information entry.

## Slide 6
2.6 - When the audiogram creation process is finished, click the Fitting section above.
2. Customer information entry.

## Slide 7
2.7 - If you have connected the device without any problems, the software will automatically select the device. Click OK and continue.
2. Customer information entry.

## Slide 8
3.1– You can see the model and serial number of the device you have connected to the software on this page.
3. Adjust the Hearing Aid.

## Slide 9
3.2 - The device you connect to the software BTE-P series, this device has 4 environmental listening program options. You can program separately by choosing the program you want.
3. Adjust the Hearing Aid.

## Slide 10
3.3 - We recommend that you use the Auto Fitting function first when starting programming. When the audiogram is entered, it will automatically make the most appropriate adjustment according to the audiogram. Click Execute.
3. Adjust the Hearing Aid.

## Slide 11
3.4 - If you want to automatically adjust for a specific problem, you can use the Intelligent Fitting function. To do this, select the problem you are having trouble with and click Execute.
3. Adjust the Hearing Aid.

## Slide 12
3.5 - If you want to increase or decrease the volume of the device without changing the audiogram diffraction of the device, you can increase or decrease the volume by clicking the up and down arrows.
3. Adjust the Hearing Aid.

## Slide 13
3.6 - If you get a whistling sound known as “feedback” on the device whose volume you increase, you can solve this problem by using the SIW function.
3. Adjust the Hearing Aid.

## Slide 14
3.7 - After repeating these steps in other environment programs, after programming each one, click the Fitting Section to make more detailed and fine-tuning.
3. Adjust the Hearing Aid.

## Slide 15
3.8 - You can start with channel adjusting by clicking Channel section.
3. Adjust the Hearing Aid.

## Slide 16
3.9 - You can click numbers on the below table and increase or decrease by using +1,-1,+3 and -3.
3. Adjust the Hearing Aid.

## Slide 17
3.10 - You can click numbers on the below table and increase or decrease by using +1,-1,+3 and -3.
3. Adjust the Hearing Aid.

## Slide 18
3.11 - Then you can adjust band by clicking Band section.
3. Adjust the Hearing Aid.

## Slide 19
3.12 - To see all the frequencies you should click arrow below.
3. Adjust the Hearing Aid.

## Slide 20
3.13 - You can click little one or more than one boxes on the frequencies and adjust by using up and down arrows or your mouse.
3. Adjust the Hearing Aid.

## Slide 21
3.13 – Finally you can click Advanced section to make advanced adjustments.
3. Adjust the Hearing Aid.

## Slide 22
3.13 – Finally you can click Advanced section to make advanced adjustments. And you should repeat all the adjustments for each environmental program.
3. Adjust the Hearing Aid.

## Slide 23
3.13 – When you finish all the adjustments, click to Load then you will complete the fitting.
3. Adjust the Hearing Aid.

## Slide 24
Thank you！